## Slide 1: Orthogonal Codes for Acoustic Underwater Localization
Sergej Keller

## Slide 2: Content
Motivation
Concept
Codes
Signal processing
Localization
Results
Conclusion
2

## Slide 3: Motivation
Acoustic transmission
  Underwater communication
  Electromagnetic waves not applicable
Autonomous diving, underwater navigation
  Self-localization
  Reverse method of classic approach
3
anchors
distances

## Slide 4: Concept
Acoustic signals from anchors
  Send synchronized by hydrophones
  Challenges like multipath propagation & noise
Time Difference of Arrival (TDOA)
  Correlation technique to estimate position
  Works great with orthogonal codes
Orthogonal PN codes
  Separable signals
  Already in use in telecommunications
4
time
anchor

## Slide 5: Orthogonal PN codes – overview
5
Code and signal length
Code length N, signal length M
Code properties
Auto-correlation properties  improved peaks in correlation
Cross-correlation  better separability, less cross talking
m-sequences
Gold codes
Kasami codes

## Slide 6: Orthogonal PN codes – evaluation results
6
Evaluation results
M-sequences have worst separability
Gold codes and Kasami codes are on the same level
Gold codes chosen because of larger sets  scalability of anchors
Evaluation parameters
Peak to Sidelobe Ratio (PSR)  increases with peak clarity
Autocorrelation to Cross-correlation Ratio (ACR)  increases with code separability, orthogonality
Gold codes

## Slide 7: Signal processing – sending & receiving
Sending signal
Binary code converted to signed
up sampled & applied FIR filter
Shifted to transfer-band for transmission
receiving signal
Sum of signals filtered & back shifted to baseband
Second filter removing shifting characteristics
Cross correlation with original signals
7

## Slide 8: Peak detection – CA-CFAR
Localization procedure
Cell Averaging – Constant False Alarm Rate
2 bins: guard and train
  Guard cells increases threshold around peaks
  train cells get an estimate of the sidelobes
  Scaled by factor S, the resulting threshold decides between peak or false alarm
8
[Hermann Rohling. Ordered statistic cfar technique - an overview. In 2011 12th International Radar Symposium (IRS), page 635, 2011]
Alternative cell measure
Ordered Statistics – Constant False Alarm Rate
Using median instead of averaging
Not used in project

## Slide 9: Localization
9
Localization algorithm
hyperbolic position location technique by TDOA
For N dimensions N+1 beacons needed
[Ralph Bucher and Durga Misra. A synthesizable vhdl model of the exact solution for three-dimensional hyperbolic positioning system. VLSI Design, 15, 2002]
time
anchor

## Slide 10: Localization
10
Localization algorithm
hyperbolic position location technique by TDOA
For N dimensions N+1 beacons needed
Used in GPS
Creates 2 candidates for position
Candidate selection
  Environmental information
  Conclusions based on previous position
[Ralph Bucher and Durga Misra. A synthesizable vhdl model of the exact solution for three-dimensional hyperbolic positioning system. VLSI Design, 15, 2002]
anchors
candidates

## Slide 11: Simulation
Simulation process
Delays, calculated from example coordinates, add to signals
Delayed signals get summed up
To the sum a by SNR adjustable noise gets added
Additional Watermark simulation
  Uses different channels
  Convolution by Dirac comb
11
H[s]

## Slide 12: Simulation – results
20 dB
-5 dB
For simulation, a circular path & corresponding TDOA are generated
4 anchors placed above spanning a rectangular shape
Different levels of noise and Watermark channels PLANE1 and CASTLE2 used
Increasing noise highly rise the risk of false detection of peaks and therefore unreliable position data
12

## Slide 13: Simulation – results
For simulation, a circular path & corresponding TDOA are generated
4 anchors placed above spanning a rectangular shape
Different levels of noise and Watermark channels PLANE1 and CASTLE2 used
Increasing noise highly rise the risk of false detection of peaks and therefore unreliable position data
13
CASTLE2, -5dB
PLANE1, -5dB
[P. van Walree, R. Otnes, and T. Jenserud, Watermark: A realistic benchmark for underwater acoustic modems, in 2016 IEEE Third Underwater Communications and Networking Conference (UComms), Aug 2016]

## Slide 14: Real world setup
Field test at shoreline location with 3 hydrophones deployed at 1 m depth, third used for receiving
2 signal generating oscilloscopes synchronized
Underwater speed of sound measured to be 1430.3 using CTD Sensor
Test runs done with code degrees of 10, 9, and 8, repeated with decreased signal intensity for lower SNRs
14
anchor | distance to R | distance to R’
A | 4.1 m | 9.66 m
B | 10.74 m | 16.3 m

## Slide 15: Real world setup - results
15
10th deg. code with high SNR
10th deg. code with low SNR
9th deg. code with high SNR
9th deg. code with low SNR
signals of 51ms vs 2.5ms length (10th vs 9th deg. code)
Values vary by 10cm
Decreased SNR shifts the position overall
Highest code degree most suitable
Algorithm yields satisfactory results

## Slide 16: Conclusion
Project work results
Optimal orthogonal pseudorandom code gold codes selected for satisfactory properties
3D position localization algorithm developed & effectively simulated with 4 anchors
Code of 10th deg. yields usable results even with low SNR
Implementation in python
Objectives of improvement
CA-CFAR algorithm effective for peak detection but needs improvement
Room for improvement by alternative CFAR algorithm (OS-CFAR) & exploration of other peak detection methods
Future research of evaluating 3d position performance in real-world scenarios.
16

## Slide 17: Literature and sources
Hermann Rohling. Ordered statistic cfar technique - an overview. In 2011 12th International Radar Symposium (IRS), page 635, 2011
Ralph Bucher and Durga Misra. A synthesizable vhdl model of the exact solution for three-dimensional hyperbolic positioning system. VLSI Design, 15, 2002
P. van Walree, R. Otnes, and T. Jenserud, Watermark: A realistic benchmark for underwater acoustic modems, in 2016 IEEE Third Underwater Communications and Networking Conference (UComms), Aug 2016
17

## Slide 18: Thanks for your patience! Questions?

## Slide 19: Simulation – results: -5dB and 20dB level noise

## Slide 20: Simulation – results: -5dB and 20dB level noise + channels

## Slide 21: Codes: evaluation

## Slide 22: Simulation – results: relation between SNR and error

## Slide 23: Simulation – results: relation between SNR and error (alt)

## Slide 24: Bode plots of Butterworth (5th order)

## Slide 25: Real world testing: degree of 8